## Slide 1: .crash course
Christina Protopapadaki, Filip Jorissen & Bram van der Heijde
Christina.Protopapadaki@bwk.kuleuven.be Filip.Jorissen@mech.kuleuven.be,
Bram.vanderHeijde@kuleuven.be
October 19, 2017

## Slide 2: Modelica crash course
What is Modelica ?
Syntax, language concepts and model structuring
Modelica tools
Use of IDEAS library
Getting started (tutorials, reference docs, libraries, software implementations, ...)
 To get you started with Modelica!

## Slide 3
 | Agenda
13:00 - 13:30 | What is modelica? How does it work?
13:30 - 13:45 | What is Dymola and how does it work? Where to find information?
13:45 – 14:00 | Break & Licence activation
14:00 – 14:30 | What is IDEAS?
14:30 - 15:30 | IDEAS: SimpleHouse Hands-on
15:30 - 16:30 | Advanced topics
16:30 - 17:30 | Demo IDEAS Building model (optional)

## Slide 4: What is Modelica?

## Slide 5
Slide from Peter Fritzson, Introduction to Object-Oriented Modeling, Simulation and Control with Modelica, Tutorial for Modelica Conference 2011, Dresden

## Slide 6
Slide from Peter Fritzson, Introduction to Object-Oriented Modeling, Simulation and Control with Modelica, Tutorial for Modelica Conference 2011, Dresden

## Slide 7
Slide from Peter Fritzson, Introduction to Object-Oriented Modeling, Simulation and Control with Modelica, Tutorial for Modelica Conference 2011, Dresden

## Slide 8
Slide from Peter Fritzson, Introduction to Object-Oriented Modeling, Simulation and Control with Modelica, Tutorial for Modelica Conference 2011, Dresden

## Slide 9
Slide from Peter Fritzson, Introduction to Object-Oriented Modeling, Simulation and Control with Modelica, Tutorial for Modelica Conference 2011, Dresden

## Slide 10: What is Modelica
Modelica is a language for modeling of physical systems
  open source
  object oriented
  Acausal modeling (equation based)
  multi-domain
  primarily for simulation, but usable for optimization
  small and large models (> 100 000 equations)
  many model libraries (free and commercial)
  textual and graphical modeling

## Slide 11: How does Dymola work?

## Slide 12: Modelica environments
Commercial software tools
Dymola (Dassault Systèmes, Sweden)
MathModelica (MathCore, Sweden)
SimulationX (ITI, Germany)
MapleSim (Maplesoft, Canada)
Free and open source tools
OpenModelica (Open Source Modelica Consortium, Sweden and other countries)
JModelica (Modelon, Sweden)

## Slide 13: What does Dymola do?
Compiles and integrates equations
  Finds solution to ODEs at indicated times
  
  Different solvers
    Radau, Dassl, Euler, Runge-Kutta,…
    Define start and end time, time step
    Define Solver tolerance
Simulates model
Plots output

## Slide 14: Graphical user interface

## Slide 15: Graphical user interface

## Slide 16: Graphical user interface

## Slide 17: Graphical user interface

## Slide 18: Break
Time to activate and borrow your license!

## Slide 19: Use of Dymola with KULeuven license
Access to a floating licence (on the building physics server).
Connected physically (cable) to the building physics or mech network
Open Dymola and go to help>licence..
Enter 10.112.72.4 and follow instructions
More information on Modelicans (google groups)

## Slide 20: How does Modelica work?

## Slide 21: Equations
Arithmetic operators
  *, /, +, -, ^ (use . for element-wise)
Derivatives
  der(x) = x ~
Slide from Peter Fritzson, Introduction to Object-Oriented Modeling, Simulation and Control with Modelica, Tutorial for Modelica Conference 2011, Dresden
Notes: Modelica is a programming language. Overview of the most important parts of the syntax

## Slide 22: Logical operators, control flow
Logical
  and, or, not
Conditional
  if, elseif, else
Loops
  for
Comparing numbers
  >, <, <>, >=,…

## Slide 23: Models
From M. Tiller, Modelica by Example, http://book.xogeny.com
# variables = # equations!
Balanced
Close line with ;

## Slide 24: Comments
Very important!
Comments regarding components, parameters, variables
  “this is a comment”
  Can show up in graphical interface
Line comments
  // This is a comment on one line
  /* This is a comment over multiple lines */

## Slide 25
Slide from Peter Fritzson, Introduction to Object-Oriented Modeling, Simulation and Control with Modelica, Tutorial for Modelica Conference 2011, Dresden

## Slide 26: Connectors
Usually
  Signal in out
  Fluid flow (mass flow rate, pressure, enthalpy)
  Heat flow (heat flow rate, temperature)

## Slide 27: Connectors
flow variable, potential variable
  Potential: voltage, pressure, temperature…
  Flow: current, mass/volume flow, heat flow…
Example: Electrical model
Slide from Peter Fritzson, Introduction to Object-Oriented Modeling, Simulation and Control with Modelica, Tutorial for Modelica Conference 2011, Dresden

## Slide 28: Components
Instances of a model
model name usually Capitalized, instance not
  Wall innerWall(res = 200, A = 10);
public variables and parameters can be accessed with dot notation, e.g.:
  heatPort.Qflow
  wall.res
Protected variables/params cannot be accessed
  Don’t show up in simulation results

## Slide 29: Homework exercise

## Slide 30: ToDo BRAM: add slides on homework example and link to inheritance

## Slide 31: Inheritance
Model inherits from other model
  Variables, parameters, equations
partial model
Code can be managed more easily
Example

## Slide 32: Interface with other programs
Scripting
  Parameter variation
  Parallel simulations
  Optimal control
Python scripts
  Nice for plotting
  BuildingsPy (http://simulationresearch.lbl.gov/modelica/buildingspy/)
  Built-in interface
MATLAB
  Built-in with Dymola

## Slide 33: Websites
General
www.modelica.org
www.openmodelica.org
www.jmodelica.org
http://www.claytex.com/tech-blog/
Modelica language
http://modref.xogeny.com/ !!!
http://book.xogeny.com/ !!!
KUL modeling conventions
https://docs.google.com/document/d/1MaNKTdLz-YPpEEH3Eg12ECzG0ErK-rIK9IHd6gsBp7Q/edit?usp=sharing
Libraries:
https://github.com/open-ideas --> IDEAS + Crash Course
https://simulationresearch.lbl.gov/modelica --> look at Buildings.Examples.Tutorial
IBPSA Project 1: https://github.com/ibpsa/modelica-ibpsa
Dymola user guide
Volume 1 & 2: C:\Program Files (x86)\Dymola 2017\Documentation\Dymola User Manual Volume 1 or via Dymola > help.

## Slide 34: Fora
http://www.openmodelica.org/index.php/forum
http://www.jmodelica.org/forum
www.stackoverflow.com (tag Modelica)
And last but not least: https://groups.google.com/d/forum/modelicans