## Slide 1: .crash course
Christina Protopapadaki, Filip Jorissen & Bram van der Heijde
Christina.Protopapadaki@bwk.kuleuven.be Filip.Jorissen@mech.kuleuven.be,
Bram.vanderHeijde@kuleuven.be
October 20, 2017

## Slide 2: Modelica crash course
What is Modelica ?
Syntax, language concepts and model structuring
Modelica tools
Use of IDEAS library
Getting started (tutorials, reference docs, libraries, software implementations, ...)
 To get you started with Modelica!

## Slide 3: What is Modelica?

## Slide 4: What is Modelica
Modelica is a language for modeling of physical systems
  open source
  object oriented
  Acausal modeling (equation based)
  multi-domain
  primarily for simulation, but usable for optimization
  small and large models (> 100 000 equations)
  many model libraries (free and commercial)
  textual and graphical modeling

## Slide 5
Slide from Peter Fritzson, Introduction to Object-Oriented Modeling, Simulation and Control with Modelica, Tutorial for Modelica Conference 2011, Dresden

## Slide 6: What is Modelica?
Modeling and simulation of complex physical systems
But optimization is possible
  JModelica

## Slide 7: What is Modelica?
Language, not a tool
Tools:
  Dymola
  OpenModelica
  JModelica
Different tools
 Different GUI, workflow
 Possibly slightly different results
Check www.modelica.org for more information

## Slide 8: Multi-physics environment

## Slide 9: Modelica vs. Simulink-style
Slide from Michael Wetter and Thierry Nouidui, Introduction to Modelica (2015), see http://simulationresearch.lbl.gov/modelica/downloads/workshops/2015-06-22-lbnl/slides/modelica-intro.pdf
Notes: Slide Michael wetter

## Slide 10: Modelica vs. Simulink-style
Slide from Michael Wetter and Thierry Nouidui, Introduction to Modelica (2015), see http://simulationresearch.lbl.gov/modelica/downloads/workshops/2015-06-22-lbnl/slides/modelica-intro.pdf
What if we want to change heat injection to here?
Notes: Slide Michael wetter

## Slide 11: Modelica vs. Simulink-style
Slide from Michael Wetter and Thierry Nouidui, Introduction to Modelica (2015), see http://simulationresearch.lbl.gov/modelica/downloads/workshops/2015-06-22-lbnl/slides/modelica-intro.pdf
Notes: Slide Michael wetter

## Slide 12: How does Dymola work?

## Slide 13: Modelica environments
Commercial software tool
Dymola (Dassault Systèmes, Sweden)
Free and open source tools
OpenModelica (Open Source Modelica Consortium, Sweden and other countries)
JModelica (Modelon, Sweden)

## Slide 14: What does Dymola do?
First translates, then compiles and integrates equations
  Finds solution to ODEs at indicated times
  
  Different solvers
    Radau, Dassl, Euler, Runge-Kutta,…
    Define start and end time, time step
    Define Solver tolerance or fixed time step
Simulates model
Plots output

## Slide 15: Graphical user interface
Icon view

## Slide 16: Graphical user interface
Diagram view

## Slide 17: Graphical user interface
Documentation view

## Slide 18: Graphical user interface
Modelica Text view
Notes: icon toevoegen

## Slide 19: Graphical user interface
Simulation tab

## Slide 20: Use of Dymola with KULeuven license
Access to a floating licence (on the building physics server).
Connect to WiFi
Open Dymola and go to Help > License…
Enter 10.112.72.4 and follow instructions

## Slide 21: Modelica syntax and concepts

## Slide 22: Your first model
Notes: Define variable, define equation, define initial state

## Slide 23: Your second model
Notes: Possible to define parameters: variables of which the value is known before, but can be changed by the user
Constants are used for parameters that are not likely to change

## Slide 24: Assigning units

## Slide 25: Physical types
Define own types
Use predefined SI units
  e.g. Modelica.SIunits.Voltage

## Slide 26: Documentation
Provide info to make code readable!
Notes: types: assign unit to for example real, Boolean,…

## Slide 27: Equations
Arithmetic operators
  * / + - ^ (use . for element-wise)
Time derivatives
  der(x) = x ~
  PDEs only after discretization or using specialized functions
Acausality
Slide from Peter Fritzson, Introduction to Object-Oriented Modeling, Simulation and Control with Modelica, Tutorial for Modelica Conference 2011, Dresden
Notes: Modelica is a programming language. Overview of the most important parts of the syntax

## Slide 28: Logical operators, control flow
Logical
  and or not … (see modelica specification for more)
Conditional
  if elseif else
Loops
  for
Comparing numbers
  > < <> >= …
Check syntax!

## Slide 29: Let’s connect
Make two or more models interact
  Electrical circuit
  Building
  Car
  …
Need connectors
Source DOI: 10.4271/2007-01-0541, Simic et al.

## Slide 30: Connectors
Usually
  Signal in out
  Fluid flow (mass flow rate, pressure, enthalpy)
  Heat flow (heat flow rate, temperature)
Refer to one or more types
  Allow only connections between equal connectors
Notes: Types uitleggen => enkel juiste connecties maken

## Slide 31: Connectors
Three examples:
Variables with and without “flow”
  Flow variables
  Potential variables
  Stream variables
Slide from Peter Fritzson, Introduction to Object-Oriented Modeling, Simulation and Control with Modelica, Tutorial for Modelica Conference 2011, Dresden
Heat transfer
Temperature
Heat flow
Fluid flow
Pressure
Mass flow
Specific enthalpy flow
Electricity
Voltage
Current
Notes: eerst flow uitleggen

## Slide 32: Inheritance
Model inherits from other model
  Variables, parameters, equations
partial model ( extends)
Code can be managed more easily
Example

## Slide 33: Inheritance
Partial
TwoPort
Resistance
extends TwoPort
Capacitance
extends TwoPort
Inductance
extends TwoPort
Notes: Ander voorbeeld zoeken?

## Slide 34: Homework exercise

## Slide 35: Websites
General
www.modelica.org
www.openmodelica.org
www.jmodelica.org
http://www.claytex.com/tech-blog/
Modelica language
http://modref.xogeny.com/
http://book.xogeny.com/ !!!
Libraries:
https://github.com/open-ideas --> IDEAS + Crash Course
https://simulationresearch.lbl.gov/modelica --> look at Buildings.Examples.Tutorial
IBPSA Project 1: https://github.com/ibpsa/modelica-ibpsa
Dymola user guide
Volume 1 & 2: C:\Program Files (x86)\Dymola 2017\Documentation\Dymola User Manual Volume 1 or via Dymola > help.

## Slide 36: Forums
http://www.openmodelica.org/index.php/forum
http://www.jmodelica.org/forum
www.stackoverflow.com (tag Modelica)

## Slide 37: Modelica concepts
Part 2

## Slide 38: Modelica concepts
Busses and expandable connectors
inner/outer
Media
replaceable / redeclare
records

## Slide 39: Busses and expandable connectors
Bus
  Consists of other connectors/variables
  Explicitly declared

## Slide 41: Busses and expandable connectors
Expandable connector:
  Structure/elements derived from connections
  Consistency checked at translation

## Slide 43: Inner/outer components
“outer” model -> reference to model at higher level
“inner” model -> top level instantiation of model
Example: SimInfoManager
  only one weather data reader for all components
…
…

## Slide 44: Media
Package that contain fluid properties
  Various degrees of detail possible:
    Moist/dry air
    Pure water / glycol
    Refrigerants
  Various implementations possible:
    First-principle equations
    Tables
    Polynomials
Default Media available
Needs to be specified (consistently) for each fluid component

## Slide 45: Media

## Slide 46: Replaceable / redeclare
redeclare allows to replace a submodel in a model
  i.e. similar to a parameter, which allows to replace a numerical value in a model
Allows the creation of templates, quick and convenient prototyping
Interface (e.g. connectors and parameters) must me consistent -> “constrainedby”
Example: building template with multiple heating systems

## Slide 47: Records
Structured collection of parameters

## Slide 48: Modelica libraries

## Slide 49: Modelica libraries
Modelica components can be complex
E.g. a decent pump model can contain a few thousand lines of code, spread over multiple hierarchical levels (using “extends”)
This complexity should not be exposed to users directly
  => Modelica libraries

## Slide 50: Modelica libraries
Hierarchy:
  Modelica models can contain or extend other models
  Modelica models can be grouped in packages
  Modelica packages can be nested
  A group of nested packages is a library
For building applications:
  MSL
  IDEAS
  Buildings
  See also IBPSA project 1

## Slide 51: Modelica libraries
Goal of a library:
  Provide a consistent collection of models
  for a specific (research) domain
  that is easy to use
  and allows robust simulations
Consistent: conventions
research domain: e.g. level of detail depends on application
easy to use: intuitive parameters, connections, granularity
robust: equations, no division by zero when zero flow…
Documentation, examples, validations

## Slide 52: Library example: IDEAS
Scope:
  Building and district level energy simulations, including electrical distribution grids, district heating, HVAC and control

## Slide 53: Library example: IDEAS
Buildings package:
  Elementary models for composing building zones
  Template

## Slide 54: Library example: IDEAS

## Slide 55: Library example: IDEAS
IDEAS.Buildings.Validation.Tests.ZoneTemplateVerification
  Validation example
  Unittested
  Example of granularity

## Slide 56: Library example: IDEAS

## Slide 57: Library example: IDEAS
Availability:
  Github: https://github.com/open-ideas/IDEAS
  Use master branch
  Issue tracker: bug reports
  Documentation and examples: part of library

## Slide 58: Exercise
SimpleHouse
Use template on github

## Slide 59: Advanced concepts
Compact overview

## Slide 60: Advanced concepts
Classical tools:
  domain-specific => optimised algorithms
  same people develop models and solvers
Modelica:
  general purpose solvers
  libraries often designed for robustness, not speed
  computation time is solver and problem-dependent
  To obtain fast implementations of large models it helps to know:
    the basic algorithms of the Modelica translation tool chain, and
    relevant library design decisions!

## Slide 61: Advanced concepts
Modelica code translated into efficient and portable C code
  i.e. not interpreted at runtime like python, matlab, …
Typical Modelica tool chain steps:
  Parsing (read models in code)
  Flattening (expand model object equations)
  Tarjan’s algorithm (sort equations)
  Code generation (write C code)
  Compilation (compile C code)
  Initialization (solve initial equations)
  Simulation (continuous time integration)

## Slide 62: Advanced concepts
Tarjan’s algorithm
  Sorts equations in an order such that the can be solved sequentially, and
  identifies the smallest sets of equations that need to be solved simultaneously:
    linear algebraic loops
    non-linear algebraic loops
    …
  => Determines what equations are solved for what variables (remember: acausal modelling)

## Slide 63: Advanced concepts
Algebraic loops (coupled systems of equations):
  solved using Newton solver (requires many iterations)
  can be decoupled by introducing states
    but: introduces more overhead for time integrator
    other ‘tricks’ possible

## Slide 64: Advanced concepts
Time integrator
  explicit
    Unstable for large time steps
    Examples: Euler, Runge Kutta, Dopri
  implicit
    Requires iterations (expensive)
    Scales badly for large problems
    Examples: Dassl, LSodar, Radau
  Fixed vs variable time step

## Slide 65: Advanced concepts
Further information:
Jorissen, F., Wetter, M., & Helsen, L. (2015). Simulation Speed Analysis and Improvements of Modelica Models for Building Energy Simulation. In P. Fritzson & H. Elmqvist (Eds.), 11th International Modelica Conference (pp. 59–69). Paris: Modelica Association. http://doi.org/10.3384/ecp1511859

## Slide 66: Advanced applications
Optimal control
Scripting from command line
  Parameter variation
  Parallel simulations
Python post-processing
  Nice for plotting
  BuildingsPy (http://simulationresearch.lbl.gov/modelica/buildingspy/)
  Built-in interface
MATLAB interface
  Built-in with Dymola
External C functions

## Slide 67: Components
Instances of a model
model name usually Capitalized, instance not
  Wall innerWall(res = 200, A = 10);
public variables and parameters can be accessed with dot notation, e.g.:
  heatPort.Qflow
  wall.res
Protected variables/params cannot be accessed
  Don’t show up in simulation results
Notes: Naar deel libraries?  Filip